# 1. DAC
This device is using AD9117 dual 14 bit DAC. The digital data is provided using a parallel digital input port.
AD9117 Pin Configuration

Supply voltage can be in range from 1.8 to 3.3V, in this project it is power from 3.3V. The clock supply is also be power from 3.3V rail. Additionaly the internal LDO will be used to provide 1.8V for the digital core – so the DVDD pin will be baypass with an 1uF capacitor.
A clock signal is generated using a SIT5002 100MHz CMOS clock generator. The clock ic electrical characteristics are shown bellow. The DAC also requires and DCLKIO signal which transition indicates that the IC can read the data from its inputs – the edge indicates to which DAC the input data will be send. The DCLKIO signal will be provided out of the microcontroller.

SI5002 Electrical characteristics

The AD9117 is a current DAC and it has a build in internal 62.5Ohm resistor on RLQN and RLQP (for the second chanel those pins are RLIP and RLIN). Tying the output signal to those pins will make the DAC work as a voltage output DAC. This project will include a high speed amplifier on the DAC output to buffer the output signal. The output configuration will be describe below.

A SPI is used to configure the DAC, this interace consists of Chip Select pin (CS), clock (SCLK) and data input and output pin (SDIO). After a reset the AD9117 is set at MSB first write (the communication schema is shown bellow). The ic can also be set to operate without ever writing to the serial port but this configuration will not be used in this project.

Communication schema:

This project will use only one supply voltage – 3.3V, the DAC has a build in LDO which will generate 1.8V for the digital core. Using the LDO requires a 10uF capacitor on the DVDD pin.
Output Op Amp configuration:
The output of the DAC is pass through and AD8021 200MHz (G=-1) op amp in a configuration shown below. It is based on AD9117 Figure 103. The Rs resistors should be set to 0Ohm according to the datasheet. The R_FB and RB are set to 10kOhm so the whole op amp will work as an buffer with the peak value equal to 2*Vref according to formula shown bellow:
Single-Supply configuration from AD9117 datasheet

Output amplifier configuration

AD8021 connection diagram	AD8021 frequency response

# DAC initialization
To make the DAC module work properly in this projects its registers are set to:
1. SPI Control
  No change, this settings affects only the communication protocol.
2. Power Down
  LDOOFF[0x80] = 0. LDO is set on.
  LDOSTAT[0x40] = 1. This bit only indicates when the LDO is on.
  PWRDN[0x20] = 0. All analog, digital and SPI logic are power on.
  Q DACOFF[0x10] = 1. The Q channel is not used and its turn off.
  I DACOFF[0x08] = 0. The I channel is turn on.
  QCLKOFF[0x04] = 1. The Q channel is not used and its clock is turn off.
  ICLKOFF[0x02] = 0. The I channel clock is turn on.
  EXTREF[0x01] = 0. The internal reference is turn on.
  The Power Down register is set to 0x54.
3. Data Control
  The default setting is that the I data is latched on the DCLKIO rising edge.
4. I DAC Gain
  This registers set the full-scale current as shown on a plot below:
5. IRSET
  The external 4kOhm resistor on the FSADJ pin is used to set I full-scale current output. This option is select as a default.
6. IRCML
  The external 0Ohm resistor will be used in this project
7. Q DAC Gain
  The Q DAC is not used
8. QRSET
  The Q DAC is not used
9. QRCML
  The Q DAC is not used
10. AUXDAC Q
  The Aux DAC is not used
11. AUX CTLQ
  The AUXDAQ is turn off by default.
12. AUXDAC I
  The Aux DAC is not used
13. AUX CTLI
  The AUXDAI is turn off by default.
14. Reference Resistor
  This setting affects the Vref in a way shown on a Figure below. This project will require Vref=1V, which is set by default.
15. Cal Control
  For the initialization self-calibration will not be used.
16. Call Memory
  This register shows the status of the callibration.
17. Memory Address
  This registor is not needed for the initialization of the DAC.
18. Memory Data
  This registor is not needed for the initialization of the DAC.
19. CLKMODE
  The default settings will be used.
20. Version
  Hardware version of the device, it can not be set.

[7 12 2014] The SiM3U167 microcontoller board will be replaced with ST Nucleo FT411RE board because the controller included in this module can be clocked up to 100MHz, and its an ARM-M4F with includes some DSP capability. DSP instruction will make the calculation faster so its posible to achieve higher cut-off frequency filter. The SiM3U167 can be clock up to 80MHz and doesnt include the DSP functions because its ARM-M3.